## Slide 1: Santa Fe’s 4-8-4s & HO Models
John A. Thompson
March 19, 2016

## Slide 2: Santa Fe 4-8-4 Classes and Topics
3751 Class – 14 Locos – Built in 1927-29
Major Rebuilds of 3751 Locos in 1938-39 and 1941
3765 Class – 11 Locos –Built in 1938
3776 Class – 10 Locos – Built in 1941
2900 Class – 30 Locos – Built in 1943-44

## Slide 3: 3751 Class – as Built
3751-3764 – 14 Locos – Delivered in 1927-29
73” Spoked drivers, slab rods
15K Coal tenders
Elesco feedwater heater on pilot
3751 only: steam pipe to cab was hidden
3764 only: had Caprotti valve gear until 1934

## Slide 4: 3751 Class – Converted to Oil
1936: 4 locos (3751, 3762-64) get oil insert in same 15K tender
1937-38: All 14 locos get 20K “square” oil tenders
Can now run all the way to California

## Slide 5: 3751 Class – 10 Elesco Rebuilds
1938-39: All except 3751, 3760, 3763-64 get a major rebuild
80” Boxpok drivers, longer frame
New I-beam rods
Elesco feedwater heater up in front of stack
37” pilot truck wheels instead of 33”
1940-42: All 14 locos get “SANTA FE” on tenders

## Slide 6: 3751 Class – 4 Worthington Rebuilds
1941: Major rebuild of remaining 4 original locos (3751, 3760, 3763-64)
80” Boxpok drivers, longer frame
Similar to 1st 10 rebuilds (I-beam rods, etc.) except:
  Worthington feedwater heater (square) in front of stack
  Just one large sand box
  Wagner bypass drifting valves added

## Slide 7: 3751 Class – Rebuild 7 Elescos to Worthingtons
1945-48: 7 of 10 Elesco locos are converted to Worthington (3752, 54, 55, 58, 59, 61, 62)
Get one large sand box
Also get Wagner bypass drifting valves
But 3752 gets Franklin rotary cam poppet valves in 1948, more efficient
3753, 3756-57 keep their Elescos and other features to the end

## Slide 8: 3751 Class – More Changes
By 1938: All got flip-up stack extensions
In 1941, 1945-48: Most got telescoping stack extensions when rebuilt
  But 3751, 3759-60 got curved segmented stack extensions for Tehachapi
  3753, 3756-57 kept their flip-up stack extensions
Late 1940s: Many inherited some tapered rods from 3776 & 2900 classes
Retired in mid-1950s, saved 3751 and 3759

## Slide 9: 3751 Class – HO Models – Key Brass
Original form, 73” spoked drivers, but with later 20K square oil tender
  Good for 3760, 63, 64 from 1937-38 until rebuilt in 1941
  Good for 3752-59, 61, 62 locos from 1937-38 until rebuilt in 1938-39
  Not good for 3751, as model has steam pipe above boiler
  Models imported in 1976
First rebuild with high Elesco FWH, 80” Boxpok drivers, I-beam rods
  Good for 3753, 56, 57 from 1938-39 until 1941-45, when drifting valves were added to these 3 locos (model has no drifting valves)
  Good for 3753, 56, 57 after 1945 if you add drifting valves to model
  Good for 3752, 54, 55, 58, 59, 61, 62 until 1945-48 major rebuild
  Not good for 3751, as model has steam pipe above boiler
  Models imported in 1978, some factory painted in 1981 for 3751 (incorrect) and 3757 (correct)
No Key models of 1941, 1945-48 Worthington FWH rebuilds

## Slide 10: 3751 Class – HO Models – Hallmark Brass
1941 rebuild with Worthington FWH, 80” Boxpok drivers, large sand box, drifting valves (as applied to 3751, 60, 63, 64 in 1941, also applied to 3752, 54, 55, 58, 59, 60, 61 in 1945-48)
  But models have 2 steam pipes on top, should only have one (3751 had none)
  Models were factory painted for 3751, 58, 60, 63
  Models were expensive “super crowns,” made in 1994
1948 version of 3752 with Franklin rotary cam poppet valve gear
  But model has 2 steam pipes on top, should only have one
  “Super crown,” painted 3752, made in 1994

## Slide 11: 3751 Class – HO Models – BLI Styrene
1941 rebuild with Worthington FWH, 80” Boxpok drivers, large sand box, drifting valves (as applied to 3751, 60, 63, 64 in 1941, also applied to 3752, 54, 55, 58, 59, 60, 61 in 1945-48)
  1st run 2004 – painted dark gray for 3751, 55, 62, wrong parts on pilot deck
  2nd run 2005 – painted black for 3751, 53, 56, 57, fixed pilot deck, but 3753, 56, 57 are incorrect numbers (never rebuilt this way)
  Current run 2013 – painted black for 3751, 54, 55, 60, 62, 63, 64
  All models have correct steam pipe (one, and none visible on 3751)
  See 2005 handout on details of these models

## Slide 12: 3765 Class – as Built
3765-75 – 11 locos – delivered in 1938
80” Disc drivers (with ribs), I-beam rods
20K “square” oil tenders
Worthington feedwater heater (square) in front of stack
Single sand box, paired steam pipes to cab
Unshielded water pump on right pilot deck
3765 was supposed to be streamlined, but it would have been too heavy (kept a few minor features)

## Slide 13: 3765 Class - Upgrades
1940-42: Added “SANTA FE” lettering to tenders
1944-45: Telescoping stack extensions, move check valves higher up on boiler, move whistle forward
1950-52: Most got new boilers with no steam dome but with external steam pipes (all except 3765, 3769-70)
1950s: Some got tapered rods and/or unmatched wheel types
Retired in late 1950s, saved 3768

## Slide 14: 3765 Class- HO Models – Key Brass
Imported in 1978
Modeled after 3768 as preserved, with new boiler and no steam dome
Good for most of class (but not 3765, 69, 70) after boiler replacements in Oct. 1950 - Jan. 1952 (see Worley)

## Slide 15: 3765 Class- HO Models – Hallmark Brass
Imported as Super Crowns in 1995
Painted for 3765, 3770 as built, with steam dome
  These never got new boilers, so good for entire life
  Model of 3765 has rounded cab windows, stainless steel handrails, and solid pilot, as it should (it was intended to be streamlined)
Painted for 3766, 68, 72, 74 with no steam dome (good after new boilers added in 1951)

## Slide 16: 3776 Class – as Built
3776-3785 – 10 Locos – Delivered in 1941
80” Baldwin Disc drivers with lips around holes and no ribs
Tapered rods on most, but 3784-85 had thin roller-bearing rods
Roughly similar to 3765 Class, except for:
  24.5K long oil tenders
  Whistle behind sand dome
  Two blow-downs on each side of firebox (instead of one)

## Slide 17: 3776 Class - Upgrades
Pre-1945: Add telescoping stack extensions
1946-48: Replaced tapered rods with roller-bearing rods on the other 8 locos (3784-85 already had them)
1949-52: Most got new boilers with no steam dome but with external steam pipes (all except 3777, 3781, 3783, 3785)
Retired in late 1950s, none saved

## Slide 18: 3776 Class - HO Models – PFM Brass
Many releases from 1963 through 1982, upgrades in details, some with stack up
As delivered in 1941 with tapered rods (except 3784, 85)
3784, 85 as delivered in 1941 with roller-bearing rods, and rest of class as upgraded in 1947-48 with roller-bearing rods
No models with new boiler and no steam dome (applied to most of class except 3777, 81, 83, 85 in 1950-52) (see Worley)

## Slide 19: 3776 Class – HO Models – Hallmark Brass
Imported in 1994 as Super Crowns
Painted for 3776 with no steam dome (after 1-1950)
Painted for 3779 with no steam dome (after 4-1951)
Painted for 3778, roller-bearing rods, no steam dome (after 3-1950)
Painted for 3780, roller-bearing rods, no steam dome (after 11-1952)
Painted for 3782, roller-bearing rods, no steam dome (after 11-1949)
Painted for 3783 with steam dome
Painted for 3784, roller-bearing rods, no steam dome (after 3-1952)
Painted for 3785, roller-bearing rods, with steam dome

## Slide 20: 3776 Class – HO Models – Bachmann Styrene
Many releases over the years, didn’t run well, improvements made
Some models had tapered rods, others had roller-bearing rods, all had steam dome
Factory painted for various numbers

## Slide 21: 2900 Class – as Built
2900-2929 – 30 Locos – Delivered in 1943-44
80” Boxpok drivers, tapered rods
Heaviest 4-8-4s for any railroad (heavier wartime steel)
24.5K long oil tenders
Almost identical to 3776 Class, except for:
Single blow-down on each side of firebox, domed-end air tanks, whistle behind stack, lighter crosshead without counterbalance

## Slide 22: 2900 Class - Upgrades
1946-48: Replaced tapered rods with roller-bearing rods on all locos, changed rear driver to 1941 Baldwin Disc type (raised lip around holes), added extension stacks
By 1950: Add twin sealed-beam headlights to 3 locos (2905, 2919-20)
Never got new boilers
Retired in late 1950s, saved 2903, 2912, 2913, 2921, 2925, 2926

## Slide 23: 2900 Class – HO Models – Westside Brass
Imported in 1978 as part of Fleetwood “Big Three” set of three models in wood box (3460 class, 2900 class, 5001 class)
As built with tapered rods (good until 1947-48 change to roller-bearing rods)
Note: River Point Station planned to make brass 3765, 3776, and 2900 models, but project is still on hold

## Slide 24: 2900 Class – HO Models – Hallmark Brass
Imported in 1994 as Super Crowns, with stack up
Painted 2900 as built with tapered rods (good until 1947-48)
Painted 2903 with roller bearing rods (after 1947-48)
Painted 2909 with roller bearing rods (after 1947-48)
Painted 2918 with roller bearing rods (after 1947-48)
Painted 2921 with roller bearing rods (after 1947-48)
Painted 2929 as built with tapered rods (good until 1947-48)

## Slide 25: Restoration of 3751 to Operation
Moved from display in San Bernardino in 1986
Restored to operating condition during 1986-1991 at California Steel Industries in Fontana, CA
Work done by the San Bernardino Railroad Historical Society
Operated for the first time in 1991, has pulled fan trips ever since
Note: 2926 is now being slowly restored in Albuquerque

## Slide 26: Major Sources
Books:
  Iron Horses of the Santa Fe Trail, by E.D. Worley, 1965
  The Illustrated Guide to Santa Fe HO Brass Steam Locomotives, Second Edition, by Stephen L. Redding, 2003
  Santa Fe Locomotive Development, by Larry E. Brasher, 2006
  Santa Fe Northern 4-8-4 Pictorial, by Duane Karam Jr. & Jeff Ainsworth, 2000
  Evolution of the Santa Fe 4-8-4, by Jeff Ainsworth, 2015
Articles:
  Santa Fe’s 3765 Class Northerns, by Lee Berglund, Railroad Modeler, Oct. 1974
  2900 Class Northerns – Santa Fe’s War Babies, by Loren Martens & Michael A. Martin, Santa Fe Route, Vol I, No II and Vol II, No I
  Thirty Years of 4-8-4s (Santa Fe), by Lloyd E. Stagner, Trains, Feb. 1987
  A History of the 3751 Class – Santa Fe’s Big Mountains, by Loren Martens, Santa Fe Route, Vol VI, No IV and Vol VII, No I
Correspondence with Stan Kistler in 2005 to check all facts